## Slide 1: Speed, Wavelength, Frequency
System | Frequency | Wavelength
AC current | 60 Hz | 5,000 km
FM radio | 100 MHz | 3 m
Cellular | 800 MHz | 37.5 cm
Ka band satellite | 20 GHz | 15 mm
Ultraviolet light | 1015 Hz | 10-7 m
Light speed = 3 x 108 m/s = 300,000 km/s
Velocity of light = Frequency x Wavelength (C=λν)

## Slide 2: Typical electromagnetic properties

## Slide 3: Propagation Mechanisms
Reflection
  Propagation wave impinges on an object which is large as compared to wavelength – (Cellular - 900MHz –wavelength- 37.5 cms)
- e.g., the surface of the Earth, buildings, walls, etc.
Diffraction
  Radio path between transmitter and receiver obstructed by surface with sharp irregular edges
  Waves beyond around the obstacle, even when LOS (line of sight) does not exist
Scattering
  Objects smaller than the wavelength of the propagation wave
- e.g. foliage, street signs, lamp posts

## Slide 4: Radio Propagation Effects
Transmitter
d
Receiver
hb
hm
Diffracted Signal
Reflected Signal
Direct Signal
Building

## Slide 5: Fading
Small Scale fading
  Instantaneous received power variation
  Delay spread
  Doppler spread
Large scale fading
  Path loss
  Shadowing
  Obstacles

## Slide 6: Free-space Propagation Model
The received signal power at distance d:
where Pt is transmitting power, Ae is effective area, and Gt is the transmitting antenna gain. Assuming that the radiated power is uniformly distributed over the surface of the sphere.
Transmitter
Distance d
Receiver
hb
hm

## Slide 7: Free-space Propagation Model (contd.)

## Slide 9: Antenna Gain
For a circular reflector antenna
Gain G =  (  D /  )2
 = net efficiency (depends on the electric field distribution over the antenna aperture, losses, ohmic heating , typically 0.55)
D = diameter
thus, G =  ( D f /c )2, c =  f (c is speed of light)
Example:
Antenna with diameter = 2 m, frequency = 6 GHz, wavelength = 0.05 m
G = 39.4 dB
Frequency = 14 GHz, same diameter, wavelength = 0.021 m
G = 46.9 dB
* Higher the frequency, higher the gain for the same size antenna

## Slide 10: Path loss

## Slide 11: Antenna Field Zones
The dividing line “Rule of Thumb” is
R = 2L2/
The near field or Fresnel zone is r < R
The far field or Fraunhofer zone is r > R
L= Largest linear physical dimension

## Slide 14: Ground reflection (Two-Ray) Model

## Slide 23
Outdoor and indoor propagation models,
Link budget design

## Slide 55: Indoor Multipath Propagation

## Slide 68: Large Scale Model