## Slide 1: MODULE 2 Mobile Radio Propagation: Small-Scale Fading

## Slide 3
Large scale propagation properties of wireless systems - slowly varying properties that depend primarily on the distance between Tx and Rx.
  Free space path loss
  Power decay with respect to a reference point
  The two-ray model
  General characterization of systems using the path loss exponent.
  Diffraction
  Scattering
Small signal: Rapidly changing signal characteristics primarily caused by movement and multipath.

## Slide 4: I. Fading
Fading: rapid fluctuations of received signal strength over short time intervals and/or travel distances
Caused by interference from multiple copies of Tx signal arriving @ Rx at slightly different times
Three most important effects:
  Rapid changes in signal strengths over small travel distances or short time periods.
  Changes in the frequency of signals.
  Multiple signals arriving a different times. When added together at the antenna, signals are spread out in time. This can cause a smearing of the signal and interference between bits that are received.

## Slide 5
Fading signals occur due to reflections from ground & surrounding buildings (clutter) as well as scattered signals from trees, people, towers, etc.
  often an LOS path is not available so the first multipath signal arrival is probably the desired signal (the one which traveled the shortest distance)
  allows service even when Rx is severely obstructed by surrounding clutter
Notes: fading

## Slide 6
Even stationary Tx/Rx wireless links can experience fading due to the motion of objects (cars, people, trees, etc.) in surrounding environment off of which come the reflections
Multipath signals have randomly distributed amplitudes, phases, & direction of arrival
  vector summation of (A ∠θ) @ Rx of multipath leads to constructive/destructive interference as mobile Rx moves in space with respect to time
Notes: stationary

## Slide 7
received signal strength can vary by Small-scale fading over distances of a few meter (about 7 cm at 1 GHz)!
  This is a variation between, say, 1 mW and 10-6 mW.
  If a user stops at a deeply faded point, the signal quality can be quite bad.
  However, even if a user stops, others around may still be moving and can change the fading characteristics.
  And if we have another antenna, say only 7 to 10 cm separated from the other antenna, that signal could be good.
Notes: 10^ -6 mW Antenna space diversity

## Slide 8
fading occurs around received signal strength predicted from large-scale path loss models

## Slide 9: II. Physical Factors Influencing Fading in Mobile Radio Channel (MRC)
1) Multipath Propagation
  # and strength of multipath signals
  time delay of signal arrival
    large path length differences → large differences in delay between signals
  urban area w/ many buildings distributed over large spatial scale
    large # of strong multipath signals with only a few having a large time delay
  suburb with nearby office park or shopping mall
    moderate # of strong multipath signals with small to moderate delay times
  rural → few multipath signals (LOS + ground reflection)

## Slide 10
2) Speed of Mobile
  relative motion between base station & mobile causes random frequency modulation due to Doppler shift (fd)
  Different multipath components may have different frequency shifts.
3) Speed of Surrounding Objects
  also influence Doppler shifts on multipath signals
  dominates small-scale fading if speed of objects > mobile speed
    otherwise ignored

## Slide 11
4) Tx signal bandwidth (Bs)
  The mobile radio channel (MRC) is modeled as filter w/ specific bandwidth (BW)
  The relationship between the signal BW & the MRC BW will affect fading rates and distortion, and so will determine:
    a) if small-scale fading is significant
    b) if time distortion of signal leads to inter-symbol interference (ISI)
  An MRC can cause distortion/ISI or small-scale fading, or both.
    But typically one or the other.

## Slide 12: Doppler Shift
motion causes frequency modulation due to Doppler shift (fd)
v : velocity (m/s)
λ : wavelength (m)
θ : angle between
mobile direction
and arrival direction of RF energy
        + shift → mobile moving toward S
        − shift → mobile moving away from S

## Slide 13
Two Doppler shifts to consider above
  1. The Doppler shift of the signal when it is received at the car.
  2. The Doppler shift of the signal when it bounces off the car and is received somewhere else.
Multipath signals will have different fd’s for constant v because of random arrival directions!!

## Slide 15
Note: What matters with Doppler shift is not the absolute frequency, but the shift in frequency relative to the bandwidth of a channel.
  For example: A shift of 166 Hz may be significant for a channel with a 1 kHz bandwidth.
  In general, low bit rate (low bandwidth) channels are affected by Doppler shift.

## Slide 16: Multipath parameters

## Slide 17: Received Signal strength

## Slide 18: IV. Multipath Channel Parameters
Derived from multipath power delay profiles (Eq. 5-18)
  P (τk) : relative power amplitudes of multipath signals (absolute measurements are not needed)
    Relative to the first detectable signal arriving at the Rx at τ0
  use ensemble average of many profiles in a small localized area →typically 2 − 6 m spacing of measurements→ to obtain average small-scale response

## Slide 19
    A simple way to explain this is “the range of time within which most of the delayed signals arrive”
  “excess delay” : all values computed relative to the time of first signal arrival τo

## Slide 20
Time Dispersion Parameters
  “excess delay” : all values computed relative to the time of first signal arrival τo
  mean excess delay →
  RMS delay spread →
  where Avg( τ2) is the same computation as above as used for except that
    A simple way to explain this is “the range of time within which most of the delayed signals arrive”

## Slide 21
  outdoor channel ~ on the order of microseconds
  indoor channel ~ on the order of nanoseconds

## Slide 22
Coherence BW (Bc) and Delay Spread ( )
  The Fourier Transform of multipath delay shows frequency (spectral) characteristics of the MRC
  Bc : statistical measure of frequency range where MRC response is flat
    MRC response is flat = passes all frequencies with ≈ equal gain & linear phase
    amplitudes of different frequency components are correlated
    if two sinusoids have frequency separation greater than Bc, they are affected quite differently by the channel

## Slide 23
  amplitude correlation → multipath signals have close to the same amplitude → if they are then out-of-phase they have significant destructive interference with each other (deep fades)
  so a flat fading channel is both “good” and “bad”
    Good: The MRC is like a bandpass filter and passes signals without major attenuation from the channel.
    Bad: Deep fading can occur.

## Slide 24
  so the coherence bandwidth is “the range of frequencies over which two frequency components have a strong potential for amplitude correlation.”

## Slide 25
estimates
  0.9 correlation → Bc ≈ 1 / 50 (signals are 90% correlated with each other)
  0.5 correlation → Bc ≈ 1 / 5
  specific channels require detailed analysis for a particular transmitted signal – these are just rough estimates

## Slide 26
A channel that is not a flat fading channel is called frequency selective fading because different frequencies within a signal are attenuated differently by the MRC.
  Note: The definition of flat or frequency selective fading is defined with respect to the bandwidth of the signal that is being transmitted.
  Bc and στ are related quantities that characterize time-varying nature of the MRC for multipath interference from frequency & time domain perspectives

## Slide 27
Coherence BW (Bc) and Delay Spread ( ) parameters do NOT characterize the time-varying nature of the MRC due to the mobility of the mobile and/or surrounding objects
  that is to say, Bc and characterize the statistics, (how multipath signals are formed from scattering/reflections and travel different distances)
  Bc and στ do not characterize the mobility of the Tx or Rx.
Notes: Mobility, static

## Slide 28
Doppler Spread (BD) & Coherence Time (Tc)
  BD : measure of spectral broadening of the Tx signal caused by motion → i.e., Doppler shift
    BD = max Doppler shift = fmax = vmax / λ
    In what direction does movement occur to create this worst case?
    if Tx signal bandwidth (Bs) is large such that Bs >> BD then effects of Doppler spread are NOT important so Doppler spread is only important for low bps (data rate) applications (e.g. paging)

## Slide 29
Tc : statistical measure of the time interval over which MRC impulse response remains invariant → amplitude & phase of multipath signals ≈ constant
  Coherence Time (Tc) = passes all received signals with virtually the same characteristics because the channel has not changed
  time duration over which two received signals have a strong potential for amplitude correlation
Notes: Constant

## Slide 30
  Two signals arriving with a time separation greater than Tc are affected differently by the channel, since the channel has changed within the time interval
  For digital communications coherence time and Doppler spread are related by
fm – max. Doppler spread

## Slide 31: V. Types of Small-Scale Fading
Fading can be caused by two independent MRC propagation mechanisms:
  1) time dispersion → multipath delay (Bc , )
  2) frequency dispersion → Doppler spread (BD , Tc)
    Important digital Tx signal parameters → symbol period & signal BW

## Slide 32
A pulse can be more than two levels, however, so each period would be called a "symbol period".
  We send 0 (say +1 Volt) or 1 (say -1 Volt) → one bit per “symbol”
  Or we could send 10 (+3 Volts) or 00 (+1 Volt) or 01 (-1 Volt) or 11 (-3 Volts) → two bits per “symbol”

## Slide 33: Types of small-scale fading

## Slide 34
Fading due to Multipath Delay
  A）Flat Fading → Bs << Bc or Ts >>
    signal fits easily within the bandwidth of the channel
    channel BW >> signal BW
    most commonly occurring type of fading

## Slide 35
spectral properties of Tx signal are preserved
  signal is called a narrowband channel, since the bandwidth of the signal is narrow with respect to the channel bandwidth
  signal is not distorted
What does Ts >> mean??
  all multipath signals arrive at mobile Rx during 1 symbol period
  ∴ Little intersymbol interference occurs (no multipath components arrive late to interfere with the next symbol)

## Slide 36
flat fading is generally considered desirable
  Even though fading in amplitude occurs, the signal is not distorted
  Forward link → can increase mobile Rx gain (automatic gain control)
  Reverse link → can increase mobile Tx power (power control)
  Can use diversity techniques (described in a later lecture)

## Slide 37
B) Frequency Selective Fading → Bs > Bc or Ts <
  Bs > Bc → certain frequency components of the signal are attenuated much more than others

## Slide 38
Ts < στ → delayed versions of Tx signal arrive during different symbol periods
  e.g. receiving an LOS → “1” & multipath “0” (from prior symbol!)
  This results in intersymbol interference (ISI)
  Undesirable
it is very difficult to predict mobile Rx performance with frequency selective channels

## Slide 39
2) Fading due to Doppler Spread
  Caused by motion of Tx and Rx and reflection sources.
  A) Fast Fading → Bs < BD or Ts > Tc
  Bs < BD
    Doppler shifts significantly alter spectral BW of TX signal
    signal “spreading”
  Ts > Tc
    MRC changes within 1 symbol period
    rapid amplitude fluctuations
  uncommon in most digital communication systems

## Slide 40
B) Slow Fading → Ts << Tc or Bs >> BD
  MRC constant over many symbol periods
  slow amplitude fluctuations
  for v = 60 mph @ fc = 2 GHz → BD = 178 Hz
  ∴ Bs ≈ 2 kHz >> BD
    Bs almost always >> BD for most applications
** NOTE: Typically use a factor of 10 to designate “>>” **

## Slide 42
Rayleigh and Ricean Distributions
Rayleigh Fading Distribution
  The sum of two quadrature Gaussian noise signals

## Slide 43
Consider a carrier signal at frequency and with an amplitude
The received signal is the sum of n waves
where
define
We have

## Slide 44
It can be assumed that x and y are Gaussian random variables with mean equal to zero due to the following reasons
  n is usually very large.
  The individual amplitude are random.
  The phases have a uniform distribution.
Because x and y are independent random variables, the joint distribution p(x,y) is
The distribution can be written as a function of

## Slide 45
We have
The Rayleigh distribution has a pdf given by

## Slide 46
pdf of Rayleigh distribution

## Slide 48
Cumulative distribution function (CDF)
The mean value of the Rayleigh distribution is given by
The variance of the Rayleigh distribution is given by

## Slide 50
Ricean Fading Distribution: When there is a dominant stationary (non-fading) signal component present, such as a line-of-sight propagation path, the small-scale fading envelope distribution is Ricean.
Scattered waves
Direct wave

## Slide 51
By following similar steps described in Rayleigh distribution, we obtain
where
is the modified Bessel function of the first kind and zero-order.
The Ricean distribution is often described in terms of a parameter K which is defined as the ratio between the deterministic signal power and the variance of the multipath. It is given by or in terms of dB

## Slide 52
The parameter K is known as the Ricean factor and completely specifies the Ricean distribution.
As , we have dB. The dominant path decrease in amplitude, the Ricean distribution degenerates to a Rayleigh distribution.

## Slide 59: Parameters of a Rayleigh Fading Channel
Level Crossing Rate
Fade Rate
Average Fade Duration

## Slide 68
Average Fade Rate=

## Slide 69
Consider a Rayleigh fading signal experiencing a maximum Doppler frequency of 20 Hz. The carrier frequency is 900 MHz. Compute (a) the positive-going level-crossing rate for ρ = 1 (b) maximum velocity of the mobile for the given Doppler frequency

## Slide 70
Assume that a bit error occurs whenever any portion of a bit encounters a fade for which ρ < 0.1. For a given maximum Doppler frequency of 20 Hz,
(a) What is the average fade duration for threshold levels ρ = 0.01,ρ = 0.1,ρ = 0.707, and ρ = 1?
(b) For a binary digital modulation with a data rate of 50 bps, is the Rayleigh fading slow or fast corresponding to ρ = 0.707?
(c) What is the average number of bit errors per second for the given data rate of 50 bps?