## Slide 1: MODULE 3 Wireless Systems and Standards

## Slide 2: Contents
Introduction
GSM Architecture
GSM Channels
GSM Protocol Stack
GSM Services
GSM Handover
GSM Security

## Slide 3: Introduction

## Slide 4: Overview of Cellular System

## Slide 5: Operation of Cellular Systems
Base station (BS) at center of each cell
  Antenna, controller, transceivers
Controller handles call process
  Number of mobile units may in use at a time
BS connected to mobile telecommunications switching office (MTSO)
  One MTSO serves multiple BS
  MTSO to BS link by wire or wireless
MTSO:
  Connects calls between mobile units and from mobile to fixed telecommunications network
  Assigns voice channel
  Performs handoffs
  Monitors calls (billing)
Fully automated

## Slide 6: Channels
Control channels
  Setting up and maintaining calls
  Establish the relationship between the mobile unit and the nearest BS
Traffic channels
  Carry voice and data (generally given as two simplex channels)

## Slide 7: Call Stages

## Slide 8: Typical Call in Single MTSO Area (1)
Mobile unit initialization
  Scan and select strongest set up control channel
  Automatically selected BS antenna of cell
    Usually but not always nearest (propagation anomalies)
  Handshake to identify user and register location
  Scan repeated to allow for movement
    Change of cell
  Mobile unit monitors for pages (see below)
Mobile originated call
  Check set up channel is free
    Monitor forward channel (from BS) and wait for idle
  Send number on pre-selected channel
Paging
  MTSO attempts to connect to mobile unit
  Paging message sent to BSs depending on called mobile number
  Paging signal transmitted on set up channel

## Slide 9: Typical Call in Single MTSO Area (2)
Call accepted
  Mobile unit recognizes number on set up channel
  Responds to BS which sends response to MTSO
  MTSO sets up circuit between calling and called BSs
  MTSO selects available traffic channel within cells and notifies BSs
  BSs notify mobile unit of channel
Ongoing call
  Voice/data exchanged through respective BSs and MTSO
Handoff
  Mobile unit moves out of range of cell into range of another cell
  Traffic channel changes to one assigned to new BS
    Without interruption of service to user

## Slide 10: Other Functions
Call blocking
  During mobile-initiated call stage, if all traffic channels busy, mobile tries again
  After number of fails, busy tone returned
Call termination
  User hangs up
  MTSO informed
  Traffic channels at two BSs released
Call drop
  BS cannot maintain required signal strength
  Traffic channel dropped and MTSO informed
Calls to/from fixed and remote mobile subscriber
  MTSO connects to PSTN
  MTSO can connect mobile user and fixed subscriber via PSTN
  MTSO can connect to remote MTSO via PSTN or via dedicated lines
  Can connect mobile user in its area and remote mobile user

## Slide 11: Evolutionary Path
1G - Analog
2G -Digital
History
  1983 - 900 Systems (European)
  1987 - 1800 Systems with GSM as standard
  1991 - First System Deployed ( July)
  1992 - First GSM terminals receive interim type approval
  1993 - First GSM 1800 network launched
  1995 - GSM 1900 network in US & Canada
Specified by ETSI
  European Telecommunications Standards Institute
The primary goal is to provide voice services
  GSM is the most widely used cellular standard
  compatible with already established PSTN & ISDN
  Today’s networks are 4G, 5G, (6G)

## Slide 12: Introduction- GSM
Integration of
Tele Services
Data Services
Categories of Service
Telephone services – digital voice, SMS,
Bearer Services -data
Supplementary ISDN services- call forwarding, CUG, group calls

## Slide 13: GSM – Specifications (Specs)
Maximum cell radius (R): 35 km
Frequency: region around 900 MHz
Maximum vehicle speed (Vm):250 km/hr
Maximum coding delay: approx. 20 ms
Maximum delay spread (m): 10 s
Bandwidth: Not to exceed 200 kHz

## Slide 14: GSM – Frequency Spectra
GSM Radio frequency spectra:
  GSM 900 – Standard - Europe
  GSM 1800 - DCS ( Digital Cellular System)
  GSM 1900 - PCS ( Personal Communcation System)- US

## Slide 15: GSM uses paired radio channels
0
124
0
124
890MHz
915MHz
935MHz
960MHz
UPLINK
DOWNLINK

## Slide 16: GSM - Radio channels
Time division multiple access-TDMA
124 radio carriers, inter carrier spacing 200khz.
890 to 915 MHz mobile to base - UPLINK
935 to 960 MHz base to mobile - DOWNLINK
8 channels/carrier
GSM combines FDM and TDM: bandwidth is subdivided into channels of 200kHz, shared by up to eight stations, assigning slots for transmission on demand.
Notes: 270.833 kb/s per carrier
GMSK with a time bandwidth product BT =0.3
Slow frequency hoping 217/hops/second.
Synchronization compensation for up to 233micro seconds absolute delay
Block and convolutional channel coding copuled with interleaving to combat channel perturbations- overall channel rate of 22.8 kb/s
Full rate channel 13 kb/s voice coder rate using regular pulse excitation/linear predictive coding RPE/LPC, half rate channel 6.5 kb/s using
Vector coder rate using vector sum excited linear predictivie coding VSELP
Overall full rate channel bit rate of 22.8 kb/s.
Each cell can have from 1 to 16 pairs of carriers.

## Slide 17: Global System for Mobile Communication (GSM) Architecture

## Slide 18: Network Architecture
Base station controller

## Slide 19: GSM: Architecture
MS
MS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
PDN
ISDN, PSTN
RSS
radio cell
radio cell
MS
AUC
signaling
O
NSS
OSS
Radio subsystem
Network and
switching subsystem
Abis interface-BTS and BSC
A interface-BSC and MSC
Operation Subsystem

## Slide 20: Radio Sub System (RSS)

## Slide 21: Mobile Station
Subscriber identity module –SIM
International mobile equipment identity –IMEI
PIN

## Slide 22: Base Transceiver Station (BTS)
Handles the radio interface to the mobile station.
Consists of one or more radio terminals for transmission and reception
Each Radio terminal represents an RF Channel
TRX and MS communicates over Radio interface
Received data transcoding
Voice encryption/decryption
Signal processing functions of the radio interface
Uplink Radio channel power measurements

## Slide 23: Base Station Controller (BSC)
Provides all the control functions and physical links between the MSC and BTS (Base station)
External Interfaces
  ‘Abis’ interface towards the BTS
  ‘A’ interface towards the MSC
Monitors and controls several BTSs
Management of channels on the radio interface
Alarm Handling from the external interfaces
Performs inter-cell Handover
Switching from ‘Abis’ link to the ‘A’ link
Interface to OMC for BSS (Base station system) Management

## Slide 24: Network and Switching System- NSS

## Slide 25: Mobile Switching Center (MSC)
Performs call switching
Interface of the cellular network to PSTN
Queries HLR (home location register)when calls come from PSTN to mobile user
Inter-BSC (Base station controller) Handover
Paging
Billing

## Slide 26
Inter BSC handover

## Slide 27: Home Location Register (HLR)
Stores user data of all Subscribers related to the GMSC
  International Mobile Subscriber Identity(IMSI)
  Users telephone number (MS ISDN)
  Subscription information and services
  Reference to Authentication center for key
    Referred when call comes from public land network

## Slide 28: Visitor Location Register (VLR)
Database that contains Subscriber parameters and location information for all mobile subscribers currently located in the geographical area controlled by that VLR
Identity of Mobile Subscriber
Copy of subscriber data from HLR
Generates and allocates a Temporary Mobile Subscriber Identity(TMSI)
Location Area Code
Provides necessary data when mobile originates call

## Slide 29: Operations Subsystem

## Slide 30: Authentication Center (AuC)
Stores Subscriber authentication data called Ki, a copy of which is also stored in in the SIM card
Generates security related parameters to authorize a subscriber (SRES-Signed RESponse)
Generates unique data pattern called Cipher key (Kc) for user data encryption
Provides triplets - RAND, SRES & Kc, to the HLR on request.

## Slide 31: EIR (Equipment Identity Register)
EIR is a database that contains a list of all valid mobile station equipment within the network, where each mobile station is identified by its International Mobile Equipment Identity(IMEI).
EIR has three databases.,
  White list - For all known,good IMEI’s
  Black list - For all bad or stolen handsets
  Grey list - For handsets/IMEI’s that are on observation

## Slide 32: Global System for Mobile Communication (GSM) Channels

## Slide 33: Traffic & Control Signaling
Signaling
«bla bla bla...»
« RING ! »
riiiiing
Network
Traffic
Notes:   The network can carry two types of information:
    Traffic: this concerns all the «user to user» information. It can be voice as well as data.
    Signaling: the network also needs to carry information for its own working. The purposes of this information are numerous: traffic data routing, maintenance, security. These data are not usually visible from the user’s point of view.
  There are several signaling types:
    PTS (Per-Trunk Signaling): signaling and voice components are transmitted on the same facility. PTS requires the voice component to be completely built, even if the call can’t be completed.
    CCS (Common Channel Signaling): two separate paths are used for information transfer (one for traffic, another for all related signaling information). Thus, CCS allows the voice component to be built separately, which allows resources to be saved. For instance, no voice facilities would be assigned to the call if the dialed number is busy.
  GSM works with CCS (no. 7)

## Slide 34: Radio Link Aspects
From Speech to RF Signal
Blah… Blah… Blah...
Blah... Blah... Blah...
Digitizing and
Source Coding
Channel Coding
Interleaving
Ciphering
Burst Formatting
Modulating
Demodulating
Burst De-formatting
Deciphering
De-interleaving
Channel Decoding
Source Decoding
Notes: On the emitting end, speech frames are first coded from analog to digital (source coding) then protected (channel coding). Bits are then interleaved and grouped together in sub-blocks. These sub-blocks are distributed over several bursts modulating a carrier and then transmitted.
On the receiving end, the reverse operations are performed with an option on processing diversity.

## Slide 35: Channels : differentiating between Physical and Logical channels
Physical channels : The combination of an ARFCN (absolute radio frequency channel number) and a time slot defines a physical channel.
Logical channels : These are channels specified by GSM which are mapped on physical channels.

## Slide 36: Channel concept
Physical channel:
One timeslot of a TDMA-frame on one carrier is referred to as a physical channel.
There are 8 physical channels per carrier in GSM, channel 0-7(timeslot 0-7)
Logical channel:
A great variety of information must be transmitted between BTS and the MS, for e.g. user data and control signaling. Depending on the kind of information transmitted we refer to different logical channels.
These logical channels are mapped on physical channel.

## Slide 37: GSM - TDMA/FDD
1
2
3
4
5
6
7
8
higher GSM frame structures
935-960 MHz
124 channels (200 kHz)
downlink
890-915 MHz
124 channels (200 kHz)
uplink
frequency
time
GSM TDMA frame
GSM time-slot (normal burst)
4.615 ms
546.5 µs
tail
user data
Training
S
guard
space
S
user data
tail
guard
space
3 bits
57 bits
26 bits
57 bits
1
1
3

## Slide 38
38
38

## Slide 39
Jan 22, 2015
39
39
Speech in GSM is digitally coded at a rate of 13 kbps
456 bits every 20 ms
260 bits every 20 ms
8 57 bits block
GMSK
Convolutional Encoder
184 bits ( 20 ms)

## Slide 40: GSM Channels
GSM Channels
Control Channels
Traffic Channels
(TCHs)
Full
rate
Half
rate
Dedicated Control
Channels
(DCCHs)
Slow
Fast
Downlink
Broadcast
Channels
(BCHs)
Common Control
Channels
(CCCHs)
Downlink
Uplink
TCH /F
TCH /H
FCCH
SCH
BCCH
PCH
CBCH
RACH
AGCH
SDCCH
SACCH
FACCH
(down uplink)
Notes:   Control channels are intended to carry signaling or synchronization data. Three are defined: Broadcast Channels (BCHs), Common Control Channels (CCCHs), Dedicated Control Channels (DCCHs).
  Broadcast channels are point-to-multipoint unidirectional (downlink) control channels from the fixed subsystem to the mobile station.
    First, BCHs include a Frequency Correction Channel (FCCH) that allows an MS to accurately tune to a Base Transceiver Station (BTS).
    Then BCHs contain the Synchronization Channel (SCH), which provide TDMA frame-oriented synchronization data to an MS.
    Last, BCHs include the Broadcast Control Channel (BCCH) intended to broadcast a variety of information to MSs, including cues necessary for the MS to register in the network.

## Slide 41: Traffic Channels-TCH
TCH carries the voice data.
Two blocks of 57 bits contain voice data in the normal burst.
One TCH is allocated for every active call.
Full rate traffic channel occupies one physical channel(one TS on a carrier) and carries voice data at 13kbps
With channel coding added carries at 22.8kbps
Two half rate (6.5kbps) TCHs can share one physical channel.
User data mappped on to same time slot sent over alternate frames
With channel coding added carries at 11.4kbps

## Slide 42: Broadcast channels BCH
Broadcast Channel-BCH
  Allotted one ARFCN (absolute radio freq. channel nos.) & is ON all the time in every cell. Transmits in only TS0 and other 7 TS used by TCH.
Frequency correction channel-FCCH
  Allow the Ms local oscillator to synchronize to the BS frequency.
  Carries a 142 bit zero sequence and repeats once in every 10 frames on the BCH.
  Repeats once in every 10 frames.
Synchronization Channel-SCH (timing)
  This is used by the MS to synchronize to the TDMA frame structure within the particular cell.
  Listening to the SCH the MS receives the TDMA frame number and also the BSIC (base station identity code)( in the coded part- 39 bits).
  Repeats once in every 10 frames.

## Slide 43: Broadcast channels BCH ...
BCCH (Broadcast control channels)
  The information the MS must receive in order to receive calls or make calls -information concerning the cell (cell and network identity, channel availability and congestion).
  This include the information of Max power allowed in the cell.
  List of channels in use in the cell.
  BCCH carriers for the neighboring cells, Location Area Identity etc.
  BCCH occupies 4 frames (normal bursts) on BCH and repeats once every Multiframe.
  This is transmitted Downlink point to multipoint.

## Slide 44: Common Control Channels CCCH
Random access channel-RACH:
  Used by Mobile Station for requesting for a channel. When the mobile realizes it is paged it answers by requesting a signaling channel (SDCCH) on RACH.
  RACH is also used by the MS if it wants to originate a call.
  Uses slotted aloha access scheme

## Slide 45: Common Control Channels CCCH ..
Access Grant Channel-AGCH
  On request for a signaling channel by MS the network assigns a signaling channel(SDCCH) through AGCH. AGCH is transmitted on the downlink point to point.
Paging Channel-PCH
  The information on this channel is a paging message including the MS’s identity(IMSI/TMSI).This is transmitted on Downlink, point-to-multipoint.
  Indicates incoming calls originating from PSTN

## Slide 46: Dedicated Control Channels-DCCH
Stand alone dedicated control channel(SDCCH)
  Provides signalling services required by users
  Ensures that MS and BS remain connected while the BS and MSC verify the MS and allocate resources.
  Send authentication and alert messages
  Acts as a temporary channel that holds traffic which TCH is allocated

## Slide 47: Dedicated Control Channels-DCCH
Slow associated control channel-SACCH
  Transmission of radio link signal measurement, power control etc.
  Average signal strengths(RXLevel) and quality of service (RXQual) of the serving base station and of the neighboring cells is sent on SACCH (on uplink).
  Mobile receives information like what TX power it has to transmit and the timing advance. It is associated with TCH or SDCCH
Fast associated control channel-FACCH
  Urgent messages
  Used for Hand over commands and during call setup and release. FACCH data is sent over TCH with stealing flag set

## Slide 48: CDMA Cellular Reuse
Same Frequency is used in every cell
  Interference becomes low power noise
Spectral efficiency much higher than AMPS (Advanced Mobile Phone System).
  20 times theoretically.
  5~8 times in practice.
CDMA Design Parameters ( Same as AMPS )
  Forward Channel Frequency  869 – 894 Mhz
  Reverse Channel Frequency  824 – 849 Mhz
  Tx/Rx Frequency Spacing  45 Mhz

## Slide 49: IS-95 CDMA
Existing 12.5 Mhz assigned cellular bands are used to derive 10 different CDMA bands  1.25 Mhz per band.
Frequency Reuse factor in CDMA = 1.
Channel Rate = 1.2288 Mcps (cycles per sec).
Multipath Fading exploited in CDMA.
  Rake receivers are used to combine the output of several received signals.
  Fading does occur on the individual signals, but each signal is affected differently and so using several of them to make a decision improves the probability of obtaining a correct decision – Multipath Diversity combining.
  At Mobile
    Three correlators used to receive three different signals. With a fourth one used as a roving finger which is used to detect new strong incoming signals. Process ensures that the Rake receiver always used the three strongest signals.
  At Base Station
    All four correlators are used to receive signals  Antenna Diversity.

## Slide 50: The Rake receiver
One of the main advantages of the CDMA system is its ability to resolve different multipath components.
This is possible since CDMA is a wide band system.
In order to resolve multipath signals the subscriber unit/BTS should make use of multiple receivers
operating at different phases. Each of these receivers are called fingers.
The outputs of these fingers are added to form a strong output.
Correlator 1
Correlator 2
Correlator 3
Searcher
Combiner
Input
Correlator 1
Correlator 2
Correlator 3
Searcher
Combiner
Input
Output

## Slide 51: The Coding and Modulation process in CDMA
64 bit Walsh Codes are used to provide 64 channels within each frequency band.
Walsh codes used for spreading in the forward link.
Walsh codes used to provide orthogonal modulation and not spreading to the full 1.2288 rate in the reverse link.
Besides Walsh codes, 2 other codes are used in IS-95
  Long PN code: generated from a 42 bit shift register having (242 – 1) = 4.398 x 1012 different codes. A mask is used to overlay the codes, the mask differs from channel to channel. The chip rate is 1.2288Mcps. These codes are used for:
    Data scrambling/encryption in the forward path
    Data spreading and encryption in the reverse path
  Short PN code: generated from a pair of 15 bit shift registers having 215 –1 = 32767 codes. These codes are used for synchronization in the forward and reverse links and cell identification in the forward link
    Each cell uses one of 512 possible offsets.
    Adjacent cells must use different offsets.
    Chip Rate is 1.2288Mcps ( i.e., not used for spreading )

## Slide 52: Direct Sequence CDMA
Multiply data with a Pseudo-random noise sequence (PN)

## Slide 53
Walsh code

## Slide 54: CDMA Channels
Forward and Reverse Channels are separated by 45 Mhz.
  Forward Channel comprises of the following channels:
    Pilot channel (always uses Walsh code W0 )
    Paging channel(s) ( use Walsh code W1 – W7 )
    Sync channel (always uses Walsh code W32 )
    Traffic channels ( use Walsh codes W8 – W31 and W33 – W63 )
  Reverse Channel comprises of the following channels:
    Access channel
    Traffic channel
  Link Protocol can be summarized as follows:
    Mobile acquires phase, timing and signal strength via the Pilot channel
    Mobile synchronizes to Base Station via the Sync. Channel
    Mobile gets system parameters via the paging channel.
    Mobile and BS communicates over the traffic channels during a connection.
    Mobile and BS communicate over the access and paging channels during system acquisition and paging.

## Slide 56: Forward/Reverse Channel Spreading and Scrambling Process
Forward channels are spread using one of 64 orthogonal Walsh functions. Note – Perfect separation between the channels in the absence of multipath interference.
  To reduce interference between mobiles that use the same Walsh function in neighboring cells, all signals in a particular cell are scrambled using the the short PN sequence for cell identification.
  For the paging and traffic channels, the long PN sequence is used to scramble the signal before spreading.
Reverse channels are spread using the long PN sequence.
  All 64 orthogonal Walsh functions are used to provide orthogonal modulation.
  The stream is then scrambled using the short PN sequence for cell identification purposes.

## Slide 57: CDMA Vocoder & Transmission Rates
IS-95 supports different transmission rates. The vocoder (QCELP) (Qualcom code excited linear prediction) outputs 9.6 Kbps when there is a full speech signal and 1.2 Kbps when a silent period is detected. (Note 1)
Intermediate rates such as 4.8Kbps and 2.4 Kbps are progressively used to either increase or decrease rates based on the speech signal content.
Rate decisions are made every 20msec interval ( the interval over which samples are collected and processed).
In CDMA – A signal (rate set 1) is always sent for it takes too long for the receivers to ramp up again for reception.
However the bits are output at a correspondingly lower power. For example: the 1.2 Kbps bits are repeated 8 times to bring it up to 9.6 Kbps, but, the signal strength is reduced to 1/8 the power.
Notes: Note 1 – Studies have shown that 50% of the time there is no speech signal in one direction, and there are pauses in the speech signal

## Slide 62
General Packet Radio Service

## Slide 63: GPRS
GPRS is an expansion Global System for Mobile Communication. It is basically a packet-oriented mobile data standard on the 2G and 3G cellular communication network’s global system for mobile communication. GPRS was built up by European Telecommunications Standards Institute (ETSI)

## Slide 64
Comparison of GSM & GPRS
 | GSM | GPRS
 | Supports only voice | Supports Data over GSM
Data Rates | 9.6 Kbps | 14.4 to 171.2 Kbps
Modulation Technique | GMSK (Gaussian Minimum shift keying) | GMSK
Billing | Duration of connection | Amount of data transferred
Type of Connection | Circuit – Switched Technology | Packet - Switched Technology

## Slide 65
GPRS in INDIA
BPL Mobile
Bharti Cellular
Hutchison Max
Hutchison Essar
Idea Cellular

## Slide 66
Benefits of GPRS
New Data Services
High Speed (Data Rate 14.4 – 171.2 kbps)
Efficient use of radio bandwidth (Statistical Multiplexing)
Circuit switching & Packet Switching can be used in parallel
Constant connectivity

## Slide 67: GPRS: data transfer over GSM
Two enhancements to GSM for data
  HSCSD - High Speed Circuit Switched Data
  GPRS - General Packet Radio Service
Both have capacity to use new coding schemes and to make multislot allocation
GPRS, being a packet switched service, is known to be more efficient and flexible for data transfer purposes
It delivers circuit and packet-switched services in one mobile radio network

## Slide 68: GPRS features
Radio resources are allocated for only one or a few packets at a time, so GPRS enables
  many users to share radio resources, and allow efficient transport of packets
  fast setup/access times
  connectivity to external packet data networks
  volume-based charging
GPRS also carries SMS in data channels rather than signaling channels as in GSM

## Slide 69: Service Types
Point-to-Point
  Internet access by user
Point-to-Multipoint
  Delivery of information (e.g. news) to multiple locations or interactive conference applications

## Slide 70: QoS Profile for GPRS Bearers
Describes applications characteristics and QoS requirements
4 parameters:
  Service precedence
  Reliability parameter
  Delay parameters
  Throughput parameter
    Maximum and mean bit rates

## Slide 71: GPRS architecture
SS7
BTS
BSC
MSC
VLR
HLR
AuC
GMSC
BSS
PSTN
NSS
A
E
C
D
PSTN
Abis
B
H
MS
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
NSS Network Sub-System
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
GPRS General Packet Radio Service
IP
2G+ MS (voice & data)
PSDN
Gi
SGSN
Gr
Gb
Gs
GGSN
Gc
Gn
2G MS (voice only)

## Slide 72: GPRS architecture
Requires addition of a new class of nodes called GSNs (GPRS Support Nodes)
  SGSN: Serving GPRS Support Node,
  GGSN: Gateway GPRS Support Node
Base Station Controller requires a PCU (Packet Control Unit) and various other elements of the GSM n/w require software upgrades
All GSNs are connected via an IP-based backbone. Protocol data units (PDUs) are encapsulated and tunneled between GSNs

## Slide 73: SGSN (Serving GPRS Support Node)
Analogue of the MSC in GSM
Routes incoming and outgoing packets addressed to and from any GPRS subscriber located within the geographical area served by the SGSN
Location Register of the SGSN stores information (e.g. current cell and VLR) and user profiles (e.g. IMSI, addresses) of all GPRS users registered with this SGSN

## Slide 74: GGSN (Gateway GPRS support node)
Serves as the interface to external IP networks which see the GGSN as an IP router serving all IP addresses of the MSs
GGSN stores current SGSN address and profile of the user in its location register
It tunnels protocol data packets to and from the SGSN currently serving the MS
It also performs authentication and charging
GGSN can also include firewall and packet-filtering mechanisms

## Slide 75: BSC and others
BSC must get a Packet Control Unit to
  set up, supervise and disconnect packet-switched calls
  also support cell change, radio resource configuration and channel assignment
MSC/VLR, HLR and SMS Center must be enhanced for interworking with GPRS
MS must be equipped with the GPRS protocol stack

## Slide 76: HLR - Home Location Register
Shared database, with GSM
Is enhanced with GPRS subscriber data and routing information
For all users registered with the network, HLR keeps user profile, current SGSN and Packet Data Protocol (PDP) address(es) information
SGSN exchanges information with HLR e.g., informs HLR of the current location of the MS
When MS registers with a new SGSN, the HLR sends the user profile to the new SGSN

## Slide 77: VLR-Visitor Location Register
VLR is responsible for a group of location areas. It stores data of only those users in its area of responsibility
MSC/VLR can be enhanced with functions and register entries that allow efficient coordination between GPRS and GSM services
  combined location updates
  combined attachment procedures

## Slide 78: MS modes
Class A: MS can operate simultaneous packet switched and circuit switched services
Class B: MS can operate either one at one time
Class C: MS can operate only packet switched services

## Slide 79: Interfaces in GPRS
Control Plane
Transmission
Plane

## Slide 80: GPRS summary
Enables many users to share radio resources by dynamic, on-demand, multi-slot allocation
Provides connectivity to external packet data networks
Modification to the GSM air-interface
Addition of new GPRS Support Nodes
Assignment of PDP (Packet Data Protocol) context to MS
Enables volume-based charging as well as duration based charging

## Slide 81: UMTS-Universal Mobile Telecommunication System Core Network
The basic Core Network architecture for UMTS is based on GSM network with GPRS.
    However, all equipment has to be modified for UMTS operation and services.
The Core Network is divided in circuit switched and packet switched domains.
    Some of the circuit switched elements are (MSC), (VLR) and Gateway MSC.
    Packet switched elements are (SGSN) and (GGSN).
Some network elements, like EIR(Equipment Identity Register), HLR, and AUC are shared by both domains.

## Slide 82: UMTS- UTRAN
UMTS differs from GSM Phase 2+ mostly in the new principles for air interface transmission
    (W–CDMA instead of TDMA/ FDMA).
The UTRAN (UMTS Terrestrial Radio Access Network, based on W–CDMA )provides the air interface access method for User Equipment.
Two new network elements are introduced in UTRAN,
    RNC (Radio Network Controller) – Base station Controller
      The RNC is connected to a set of Node B elements, each of which can serve one or several cells.
    Node B (Base station)

## Slide 83: UMTS- UTRAN
The UMTS Terrestrial Radio Access System (UTRA) provides at least:
  144 kbps for full-mobility applications,
  384 kbps for limited-mobility applications,
  2.048 Mbps for low-mobility applications.

## Slide 84: UMTS architecture

## Slide 85: UMTS Architecture

## Slide 86
Media Gateway (MGW)

## Slide 87: 3G rel99 Architecture (UMTS) 3G Radio (Internet/radio access)
SS7
IP
BTS
BSC
MSC
VLR
HLR
AuC
GMSC
BSS
SGSN
GGSN
PSTN
PSDN
CN
C
D
Gc
Gr
Gn
Gi
Abis
Gs
B
H
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
RNS Radio Network System
RNC Radio Network Controller
CN Core Network
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
A
E
PSTN
2G MS (voice only)
2G+ MS (voice & data)
UMTS Universal Mobile Telecommunication System
Gb
3G UE (voice & data)
Node B
RNC
RNS
Iub
IuCS
ATM
IuPS

## Slide 88: 3G rel4 Architecture (UMTS) - Soft Switching
SS7
IP/ATM
BTS
BSC
MSC Server
VLR
HLR
AuC
GMSC server
BSS
SGSN
GGSN
PSTN
PSDN
CN
C
D
Gc
Gr
Gn
Gi
Gb
Abis
Gs
B
H
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
RNS Radio Network System
RNC Radio Network Controller
CN Core Network
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
A
Nc
2G MS (voice only)
2G+ MS (voice & data)
Node B
RNC
RNS
Iub
IuCS
IuPS
3G UE (voice & data)
Mc
CS-MGW
CS-MGW
Nb
PSTN
Mc
ATM

## Slide 89: Benefits of Media Gateways
Media gateway -translation device or service that converts media streams between different technologies such as SS7, 2G, 2.5G and 3G radio access networks) or PBX systems
Media gateways enable communications across packet networks using transport protocols such as Asynchronous Transfer Mode (ATM) and Internet Protocol (IP)
Media gateway function is to convert between different transmission and coding techniques

## Slide 90: 3G rel5 Architecture (UMTS) - IP Multimedia
Gb/IuPS
A/IuCS
SS7
IP/ATM
BTS
BSC
MSC Server
VLR
HSS
AuC
GMSC server
BSS
SGSN
GGSN
PSTN
CN
C
D
Gc
Gr
Gn
Gi
Abis
Gs
B
H
IM IP Multimedia sub-system
MRF Media Resource Function
CSCF Call State Control Function
MGCF Media Gateway Control Function (Mc=H248,Mg=SIP)
IM-MGW IP Multimedia-MGW
Nc
2G MS (voice only)
2G+ MS (voice & data)
Node B
RNC
RNS
Iub
3G UE (voice & data)
Mc
CS-MGW
CS-MGW
Nb
PSTN
Mc
IuCS
IuPS
ATM
IM
IP
PSTN
Mc
MGCF
IM-MGW
MRF
CSCF
Mg
Gs
IP Network

## Slide 91
The Core Network of UMTS is same as that of GPRS. The air interface is totally different. We therefore only discuss the air interface. The air interfaces in UMTS are listed below:
Uu: UE to Node B (UTRA, the UMTS W-CDMA air interface
Iu: RNC to GSM Phase 2+ CN interface (MSC/VLR or SGSN)
Iu-CS for circuit-switched data
Iu-PS for packet-switched data
Iub: RNC to Node B interface
Iur: RNC to RNC interface, not comparable to any interface in GSM
The Iu, Iub, and Iur interfaces are based on ATM transmission principles.

## Slide 92: What is LTE?
LTE stands for “Long Term Evolution”
Fourth-generation (4G) cellular technology from 3GPP
Deployed worldwide
4G LTE: First global standard
  Increased speed
  IP-based network (All circuits are gone/fried!)
  New air interface: OFDMA (Orthogonal Frequency-Division Multiple Access), MIMO (multiple antennas)
    Also includes duplexing, timing, carrier spacing, coding...
  New service paradigm (e.g., VoLTE)
Notes:   CAT 3, CAT 4, CAT 6 (different radio technology),  different speed
All implementations must meet baseline requirements
  Increased speed
  IP-based network (All circuits are gone/fried!)
  New air interface: OFDMA (Orthogonal Frequency-Division Multiple Access), MIMO (multiple antennas)
  Also includes duplexing, timing, carrier spacing, coding...

## Slide 93: 4G Network Architecture (LTE)
MME: Mobility Management Entity
BS: Base Station (4G: eNodeB)
4G Packet-Switched
Notes: Let us look at the mobile network architecture to see how these services are made possible.
Here it is a 4G LTE network architecture which only supports packet-switched service.
It consists of two parts:
First, base stations to offer radio access
Second, core network which consists of MME (Mobility Management Entity) and 4G PS gateways .
The MME is used to manage user mobility, e.g., location update.
The 4G PS Gateways route packets between Internet and 4G Base stations

## Slide 94: 3G/4G Network Architecture
3G Packet-Switched
4G Packet-Switched
3G Circuit-Switched
Notes: Now we take a look at 3G network architecture.
Similar to 4G LTE, it has Base station and core networks.
The major difference is that 3G supports both Circuit-Switched and Packet-Switched services.
3G CS Gateways are used to connect to 3G base stations and telephony networks.
3G PS Gateways plays role similar to 4G PS Gateway.
The main difference is that 3G PS Gateways are responsible for control-plane and data-plane functions at same.
In 4G LTE, the control-plane functions are moved to MME.

## Slide 95: Operations
Two main planes in operation in parallel:
Data plane (also called User plane): content delivery
Control plane: signaling functions
There is an additional plane that works with the above two planes:
Management plane: configurations, monitoring

## Slide 96: Illustration of Data and Control Planes
Network
Infrastructure
Data-plane
Control-
Plane
IP
Application
Transport
Data-plane
Control-
Plane
IP

## Slide 97: Illustration of Data and Control Planes
97
97
EPS: Evolved Packet System
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Control
MAC: Medium Access Control

## Slide 98: Data-Plane Protocols: IP + lower layers
Packet Data Convergence Protocol (PDCP) – header compression, radio encryption
Radio Link Control (RLC) – Readies packets to be transferred over the air interface
Medium Access Control (MAC) – Multiplexing, QoS
PDCP
RLC
@eNB (IP)
PDCP
RLC
@UE (IP)
MAC
PHY
MAC
PHY
Notes: Wireless technology, main evolution across different generations and releases are in PHY layer

## Slide 99: Control-Plane Protocols
Internet
Data-plane
Control-plane
P1: Radio conn. setup
P2: Location
update
P3: Conn.
context
(QoS)
Radio Resource Control (RRC)
Mobility Management (MM)
Connectivity Management
Control utilities: mobile network specific
  Different from Internet counterparts
Notes: It means that the network side implements complex functions.
(2) To support data delivery in the data-plane, it has to support rich control-plane functions like radio resource control, mobility support, connectivity management, QoS control etc.
(3) They are much more complex than the control in the Internet.

## Slide 100: Control-Plane Protocols in 4G/3G
Variants for same/similar control functions
  Hybrid 4G/3G systems
  Domains separated for voice (CS) and data (PS)
Notes: (1 ) Layered protocol stack
(2) Variants
(3) Complicated (rich set of control protocols)

## Slide 101: Distributed Operations: Device, base station, core networks
101

## Slide 102: Data and Control Planes in LTE
eNodeB, S-GW and P-GW are involved in session setup, handoff, routing
User Equipment (UE)
Gateway (S-GW)
Mobility Management Entity (MME)
Network Gateway
(P-GW)
Home Subscriber Server (HSS)
\Station (eNodeB)
Base Station
Serving
Packet Data
Control Plane
Data Plane

## Slide 103: LTE Architecture