## Slide 1: Orthogonal Frequency Division Modulation (OFDM)

## Slide 2: Basic Concept of OFDM
Send a sample using the entire band
Send samples concurrently using multiple orthogonal sub-channels
Wide-band channel
Multiple narrow-band channels

## Slide 3: Single Carrier Systems
Bandwidth B = 2W available for communication, where W is the one-sided bandwidth (or max freq),
For a single-carrier communication system, the symbol time T is given as T = 1/B
Symbol rate is given as

## Slide 4: Multi Carrier Systems
Divide the total bandwidth B into N sub-bands of bandwidth B/N
Subcarriers are placed at
Consider the ith subcarrier at the frequency
Let Xi denote the data transmitted on the ith subcarrier
The signal si(t) corresponding to the ith subcarrier
The N different data symbols Xi are modulated over the N different subcarriers with centre frequencies fi
Hence, there are a total of N data streams

## Slide 5: Composite Signal Transmitted and Received

## Slide 6: Composite Signal Received & Orthogonality

## Slide 7: Multi-carrier modulation transmitter

## Slide 8: Multi-carrier modulation receiver

## Slide 9: Symbol Rate of MCM system
N symbols using N subcarriers
Each with a rate B/N
Or time duration N/B
Net rate : N/(N/B)= B
Overall Symbol rate of MCM= Symbol rate of SCM
The single-carrier system transmits each symbol in time 1/B, while the MCM system transmits N symbols in parallel in time N/B

## Slide 10: Why OFDM is better? t
f
f
t
Wide-­‐band Narrow-­‐band
Multiple sub-channels (sub-carriers) carry samples sent at a lower rate
⯈ Almost same bandwidth with wide-band channel
Only some of the sub-channels are affected by interferers or multi-path effect
0 1
1 0 0
0 1
0 1 1 0 0 0 1 …........

## Slide 11: Simple Example
Consider a system with a transmission bandwidth of B = 1.024 MHz, i.e., 1024 kHz
Consider the coherence bandwidth Bc which is typically around 250 kHz, i.e., Bc ≈ 250 kHz.
Therefore, since the transmission bandwidth B >> Bc, the single-carrier system experiences frequency-selective fading and inter-symbol interference.
However, consider an OFDM system with employs N = 256 subcarriers in the same bandwidth. The bandwidth per subcarrier is Bs = 1024/ 256 = 4 kHz
B<<Bc, each channel experiences Flat fading

## Slide 12: Importance of Orthogonality
Why not just use FDM (frequency division multiplexing)
⯈ Not orthogonal
f
Individual sub-­‐channel
Leakage interference from
adjacent sub-­‐channels
f
Need guard bands between adjacent frequency bands  extra overhead and lower throughput
guard band
Guard bands protect leakage interference

## Slide 13: Multicarrier communications
Concept:
  Divide original data stream at rate R into L lower rate (R/L) streams on different carriers to increase symbol time
Effects
  High receiver complexity
    separate receiver chain per carrier
  Bandwidth due to sidebands
  Each subcarrier experiences flat fading
Bc
B/L
f
B
J. Andrews, A. Ghosh, R. Muhamed, Fundamentals of WiMAX, Prentice Hall, 2007

## Slide 14: OFDM- Basic Concept

## Slide 15: Difference between FDM and OFDM
guard band
f
Frequency division multiplexing
f
Orthogonal sub-carriers in OFDM
Don’t need guard bands

## Slide 16: Spectra of OFDM signal

## Slide 17: Modulation or Multiplexing?
OFDM can be viewed as either a modulation technique or a multiplexing technique.
  Modulation technique
    Viewed by the relation between input and output signals
  Multiplex technique
    Viewed by the output signal which is the linear sum of the modulated signals

## Slide 18: MCM to OFDM
The employment of discrete Fourier transform to replace the banks of sinusoidal generator and the demodulation significantly reduces the implementation complexity of OFDM modems.

## Slide 19: Orthogonal Frequency Division Modulation
Data coded in frequency domain
f
IFFT
* x[1]
* x[2]
…
* x[3]
t
Transformation to time domain: each frequency is a sine wave
In time, all added up
Channel frequency response
transmit
receive
Time domain signal
Frequency domain signal
FFT
Decode each subcarrier separately

## Slide 20: OFDM Transmitter and Receiver -Level 1

## Slide 21
x(t) 
 X[k]ej 2kt N kN 2
Orthogonality of Sub-carriers
IFFT
Encode: frequency-domain samples  time-domain sample
N 21
Time-domain
Frequency-domain
N tN 2
FFT
X[k] 
1
N 21
 x(t)e j 2kt N
Orthogonality of any two bins :
Decode: time-domain samples  frequency-domain sample
N 21
 e j 2kt N e j 2 pt N tN 2
 0, p  k

## Slide 22
Example
Let’s consider N=4
The signal has a symbol rate of 1 and the sampling frequency is 1 sample per symbol, so each transition is a bit
First few bits are 1, 1, -1, -1, 1, 1, 1, -1, 1, -1, -1, -1, -1, 1, -1, -1, -1, 1,…
Write these bits in rows of fours
Assume C1 is 1 Hz

## Slide 23
symbol1 | 1 | 1 | -­‐1 | -­‐1
symbol2 | 1 | 1 | 1 | -­‐1
symbol3 | 1 | -­‐1 | -­‐1 | -­‐1
symbol4 | -­‐1 | 1 | -­‐1 | -­‐1
symbol5 | -­‐1 | 1 | 1 | -­‐1
symbol6 | -­‐1 | -­‐1 | 1 | 1
bin1
bin2
bin3
bin4
t1
t2 t3 t4 t5
t6
Carrier 1 — We need to transmit 1, 1, 1 -1, -1, -1

## Slide 24
Composite Signal

## Slide 25: Example
Frequency-­‐domain signal Time-­‐domain signal
c1 c2 c3 c4
1 1 -­‐1 -­‐1
symbol1 symbol2 symbol3 symbol4
1 1 1 -­‐1
1 -­‐1 -­‐1 -­‐1
-­‐1 1 -­‐1 -­‐1
Parallel to serial conversion, and transmit time- domain samples
0, 2 -­‐ 2i, 0, 2 + 2i, 2, 0 -­‐ 2i, 2, 0 + 2i, -­‐2, 2, 2, 2, -­‐2, 0 -­‐ 2i, -­‐2,
0 + 2i, 0, -­‐2 -­‐ 2i, 0, -­‐2 + 2i, 0, -­‐2 + 2i, 0, -­‐2 -­‐ 2i, …
0 2 -­‐ 2i 0 2 + 2i
2
-­‐2
-­‐2
0 -­‐ 2i 2
2 2
0 -­‐ 2i -­‐2
0 + 2i
2
0 + 2i
IFFT

## Slide 26: Multi-Path Effect
0
0
  Line of sight path gTariene
  Pathdelay
1
1  Secondary path gain
  Secondary path delay
k
k
  Secondary path gain
  Secondary pathdelay
Faded path
Reflected multipath
y(t)  h(0)x(t)  h(1)x(t 1)  h(2)x(t  2) 
 h()x(t  )  h(t) * x(t)

time-domain
⟺
Y ( f )  H ( f )X( f )
frequency-domain
0
1
k
 
1
k

0


## Slide 27
Current symbol + delayed-version symbol
 Signals are deconstructive in only certain frequencies

## Slide 28: Frequency Selective Fading
Frequency selective fading: Only some sub-­‐carriers get aﬀected

## Slide 29: Inter Symbol Interference (ISI)
The delayed version of a symbol overlaps with the adjacent symbol
One simple solution to avoid this is to introduce a guard-band
Guard band

## Slide 30: Inter Symbol Interference
Intersymbol interference is eliminated almost completely by introducing a guard interval with zero padding in every OFDM symbol.
  Guard interval with zero padding
  The way to eliminate ISI

## Slide 31: Inter Carrier Interference
  Due to non integer number of cycles in the delayed cycle
  The way to avoid ICI – cyclic extension(works only when delay <guard time)
Guard time
FFT integration time=1/carrier spacing
Guard time
FFT integration time=1/carrier spacing
OFDM symbol time
OFDM symbol time
Subcarrier #1
Delayed subcarrier #2
Part of subcarrier #2 causing ICI on subcarrier #1

## Slide 32: OFDM symbol with cyclic extension

## Slide 33: OFDM – Two –ray multipath channel

## Slide 34: 16-QAM constellation for 48 sub-carrier OFDM link
(a) delay< guard time (b) delay(3%)>guard time
(c) delay(10%)>guard time

## Slide 35: Cyclic Prefix (CP)
However, we don’t know the delay spread exactly
⯈ The hardware doesn’t allow blank space because it needs to send out signals continuously
Solution: Cyclic Prefix
⯈ Make the symbol period longer by copying the tail and glue it in the front
Original symbol
Portion added in the front
Copy this part at front
Symbol 2
Symbol 1 Copy this part at front
Original symbol
Extension
In 802.11,
CP:data = 1:4

## Slide 36: Cyclic Prefix (CP)
Because of the usage of FFT, the signal is periodic
FFT( ) = exp(-­‐2jπΔf)*FFT( )
delayed version original signal
Delay in the time domain corresponds to rotation in the frequency domain
  Can still obtain the correct signal in the frequency domain by compensating this rotation

## Slide 37: Cyclic Prefix (CP)
original signal
w/o multipath y(t)  FFT(
) Y[k] = H[k]X[k]
w multipath
original signal + delayed-­‐version signal
y(t)  FFT(
) Y[k] = α(1+exp(-­‐2jπΔk))*X[k]
= H’[k]X[k]
Lump the phase shift in H

## Slide 38: Cyclic Prefix
Adding a cyclic prefix at transmitter leads to circular convolution
Note that misaligned timing still results in a circular convolution, just time shifted
  Makes for phase shifts in FFT bins
  Correct that in a moment
J. Andrews, A. Ghosh, R. Muhamed, Fundamentals of WiMAX, Prentice Hall, 2007

## Slide 39: OFDM Diagram-Level 2
Modulation
S/P
IFFT
P/S
Insert CP
D/A
channel
noise
+
A/D
De-mod
P/S
FFT
S/P
remove CP
Transmitter
Receiver

## Slide 40: Impact of Cyclic Prefix on Data Rate

## Slide 42: Interleaving
Forward Error Correction

## Slide 43: Pilot Insertion
Radio channels fade both in amplitude and frequency
Channel estimator – Estimate time-varying amplitude and phase of all sub-carriers
2-D channel estimator – estimate reference values based on known pilot values
By sampling theorem, Ts< Inverse of the double-sided BW of the sampled signal
Min. subcarrier spacing and min. symbol spacing between pilots
More pilots effective SNR small for data symbols

## Slide 44: Pilots – Block of 9 OFDM symbols with 16 sub-carriers

## Slide 45: Complete OFDM Transceiver

## Slide 46: Unoccupied Subcarriers
Edge sub-carriers are more vulnerable to errors under discrete FFT
⯈ Frequency might be shifted due to noise or multi-path
Leave them unused
⯈ In 802.11, only 48 of 64 bins are occupied bins
Is it really worth to use OFDM when it costs so many overheads (CP, unoccupied bins)?

## Slide 47: Synchronization
DAC (Tx)
ADC (Rx)
DAC (at Tx) and ADC (at Rx) never have exactly the sampling period
⯈ A slow shift of the symbol timing point, which rotates subcarriers
⯈ Intercarrier interference (ICI), which causes loss of the orthogonality of the subcarriers

## Slide 48: Carrier Frequency Offset (CFO)
ftx
DAC (Tx)
frx
ADC (Rx)
The oscillators of Tx and Rx are not typically tuned to identical frequencies
⯈ Up-convert baseband signal sn to passband signal yn=sn*ej2πftxnTs
⯈ Down-convert passband signal yn back to rn=sn*ej2πftxnTs*e-j2πfrxnTs=sn*ej2πfΔnTs
⯈ Error accumulates

## Slide 49: Frequency Errors
Primary sources of frequency errors
  Doppler shift
  Clock mismatches
  Phase noise
Effects
  Reduction in amplitude (missampling sinc)
  Intercarrier interference
O. Edfors, M. Sandell, J. van de Beek D. Landström, F. Sjöberg, “An Introduction to Orthogonal Frequency Division Multiplexing,” Sep 98, Available online: http://epubl.luth.se/avslutade/0347-0881/96-16/esb96rc.pdf

## Slide 50: OFDM Diagram
Modulation
S/P
IFFT
P/S
Insert CP
D/A
channel
noise
+
A/D
De-mod
P/S
FFT
S/P
remove CP
Transmitter
Receiver
Correct CFO
Phase track

## Slide 51: OFDM IFFT-FFT perspective

## Slide 52: PAPR and its Reduction Methods
PAPR – Peak to Average Power Ratio
Envelope Fluctuation – Superposition of sub-carriers
Causes Power Amplifiers to Saturate –leads to Non-linear Distortion, Inter-modulation and Out-of Band Radiation
Increased Complexity of ADC and DAC
Reduction is efficiency of RF amplifiers
BER high
Spectral Spreading – Adjacent Channel Interference (ACI) occurs
Coherent addition of N signals of same phase produces a peak which is N times the average signal.

## Slide 53: Distribution of PAPR
an – Modulating symbol
N – No. of sub-carriers
For Large N, real/imaginary value of x(t) –Gaussian distributed
Amplitude – Rayleigh Distribution
Power Distribution – chi-square distribution
With zero mean and two degrees of freedom
For a complex baseband signal

## Slide 55: Amplifier Characteristics

## Slide 56: PAPR Reduction Techniques
Distortion Techniques
  Clipping
  Peak Windowing
  Peak Cancellation
Coding
  Special FEC which exclude OFDM symbol with
  large PAPR
Scrambling
Scramble OFDM to small PAPR

## Slide 57: SC-FDMA
SC-FDMA, which stands for Single-Carrier Frequency Division Multiple Access, can be employed to reduce the peak-to-average power ratio in an OFDM system
Insertion of an N-point FFT block before the N-point IFFT block
It can then be seen that the FFT and the IFFT cancel the effect of each other and the net output is the exact input symbol stream, i.e., corresponding to a single-carrier system
This drastically reduces the PAPR
PAPR of a single-carrier system is 0 dB
Instead of using an N-point FFT, one can use an M-point FFT, where M < N, to reduce the PAPR, while still retaining the properties of the OFDM system

## Slide 59: Solved Examples
Q1. Consider a WiMAX system that operates with a total number of subcarriers N = 256, with a bandwidth of 15.625 kHz per subcarrier.
Compute the BW of the system.
If coherence BW is 250 KHz, what kind of fading will each subcarrier experience?
Compute the raw OFDM symbol time.
If WiMAX employs a cyclic prefix that is 12.5% of the symbol time, compute the duration of the cyclic prefix, the number of samples in CP, and the loss in spectral efficiency.

## Slide 62
Q2. Consider an OFDM system with total passband bandwidth B = 5 MHz with N = 512 subcarriers. The channel has a maximum delay spread of Td = 4 μs. Answer the questions that follow.
What is the symbol time of a corresponding single-carrier system?
What is the sample time of the OFDM system and the raw symbol time without the cyclic prefix?
What is the minimum number of samples required in the cyclic prefix?
If the length of the cyclic prefix is twice the required minimum calculated above, what is the total OFDM symbol time?
What is the loss in efficiency due to the overhead of the cyclic prefix?
If the modulation employed is 16-QAM, what is the effective bit rate of the above OFDM system?
At a carrier frequency of fc = 2.4 GHz, what is the maximum possible velocity of a mobile for the system to be able to function?

## Slide 64
IEEE 802.11ad is a WLAN standard operating at 60GHz. It has a much wider bandwidth than previous WLAN standards in lower-frequency bands. Four PHY formats are defined in IEEE 802.11ad, and one of them uses OFDM. The system uses a bandwidth of 1880MHz, with 512 subcarriers and a fixed 25% cyclic prefix. Now compute the following:
  What is the sample period duration assuming sampling at the Nyquist rate?
  What is the subcarrier spacing?
  What is the duration of the guard interval?
  What is the OFDM symbol period duration?
  In the standard among the 512 subcarriers, only 336 are used as data subcarriers. Assuming we use code rate 1/2 and QPSK modulation, compute the maximum data rate of the system.